## Slide 1
Recap
  SRF, DDSRF, DSOGI, MCCF, Discrete SRF
    SRF: conventional PLL – tracks changes in frequency and phase
    DDSRF: attacks the issue of unbalanced grid
    DSOGI, MCCF: deal with harmonics and unbalanced grid
  The above algorithms were studied from literature, mathematically analyzed and implemented using MATLAB Simulink
Algorithms
    SRF – Stationary to synchronous reference frame
        Loop Filter, Integrator, Closed loop system
    DDSRF – Decoupling network is the major improvement
        Enables tracking in unbalanced situation through decoupling of positive and negative sequence voltages
    DSOGI – Second order generalized integrator type filter
        Filters out the fundamental component in the stationary reference frame
    MCCF – Multiple Complex Coefficient Filters
        Requires two modules for eliminating every harmonic component
    Discrete SRF – Discretized version of the SRF PLL
        Input is sampled, transfer functions in z-domain

## Slide 2
Formulating a common convention
  All existing PLLs are modifications of the conventional SRF PLL
  Different conventions are followed in literature
  Single platform between different schemes requires a common convention
Simulation of each scheme required an in-depth understanding since mathematical models had to be re-designed to suit to our convention
Each scheme was modeled and tested individually and these models were clubbed into a single self-consistent model for comparison
Complexity involved – more than 600 comparisons!!
5 PLL schemes
SRF
DDSRF
DSOGI
5 imperfections
Unbalanced Grid
L-G Fault
Harmonics
4 variables
MCCF
Discrete SRF
Harmonics + Unbalanced Grid
Frequency Excursion
Space vector v_d
v_q
Error
Estimated angle

## Slide 3
Development of an applet (learning tool)
  Parts
    Initialization program
    Simulink models
    Intuitive program to plot
  Demo
  Importance of the applet
    Excellent tool for learning – How?
    Easy to use
    To find out which scheme tackles a particular issue better
    Additions of other schemes (if required) can be easily done
Future work
  Design optimization aimed at achieving a faster dynamic performance
  Verification of results through practical setup

## Slide 4
Thank you

## Slide 5: Synchronous Reference Frame PLL (SRF)
Situations:
Frequency Excursion
L-G Fault
Harmonics
Unbalanced Grid
Harmonics + Unbalanced Grid
Back

## Slide 6: Other PLL scheme comparisons
Situations:
Frequency Excursion
L-G Fault
Harmonics
Unbalanced Grid
Harmonics + Unbalanced Grid
Back
Discrete PLL
Situations:
Frequency Excursion
L-G Fault
Harmonics
Unbalanced Grid
Harmonics + Unbalanced Grid

## Slide 7: SRF PLL on L-G Fault
Back

## Slide 8: SRF PLL on Frequency Excursion
Back

## Slide 9: SRF PLL on Harmonics
Back

## Slide 10: SRF PLL on Unbalanced Grid
Back

## Slide 11: SRF PLL on Harmonics + Unbalanced Grid
Back

## Slide 12: DDSRF, DSOGI, MCCF on L-G Fault
Back

## Slide 13: DDSRF, DSOGI, MCCF on Unbalanced Grid
Back

## Slide 14: DDSRF, DSOGI, MCCF on Harmonics
Back

## Slide 15: DDSRF, DSOGI, MCCF on Harmonics + Unbalanced Grid
Back

## Slide 16: DDSRF, DSOGI, MCCF on Frequency Excursion
Back

## Slide 17: Discrete PLL on Frequency Excursion
Back

## Slide 18: Discrete PLL on Harmonics
Back

## Slide 19: Discrete PLL on Unbalanced Grid
Back

## Slide 20: Discrete PLL on Harmonics + Unbalanced Grid
Back

## Slide 21: Discrete PLL on L-G Fault
Back

## Slide 22: Conventional SRF PLL
Back

## Slide 23: DDSRF PLL
Back

## Slide 24: DSOGI PLL
Back

## Slide 25: MCCF PLL

## Slide 26: MCCF module (continued)
Back

## Slide 27: Discrete SRF PLL
Back

## Slide 28: Convention followed
Back

## Slide 29: Self-consistent model

## Slide 30: Grid simulator
Back