## Slide 1: The design and performance optimization of 3-phase PLLs for phase tracking under grid imperfections
Mentor: Dr. C. Nagamani
Pradhyumna R. 107108077
Sambhav R Jain 107108103
Objective:
Phase tracking
Depth of work:
Detailed analysis of 4 PLL schemes in literature (SRF, DDSRF, DSOGI, MCCF)
  Mathematical modeling
  Simulation to match results from literature
  Intuitive plot program for comparison between schemes
Novel loop filter design
  Self-consistent model based approach
  Comparisons of existing design schemes with the proposed scheme
  Development of a 3D lookup table
Experimentation (in progress)

## Slide 2: Detailed analysis of 4 PLL schemes in literature
PLL schemes developed: SRF, DDSRF, DSOGI, MCCF
  SRF – Synchronous Reference Frame PLL
  DDSRF – Decoupled Double Synchronous Reference Frame PLL
  DSOGI – Dual Second Order Generalized Integrator based 3-phase PLL
  MCCF – Multiple Complex Coefficient Filter based 3-phase PLL
Comprehensive Simulink models
Intuitive plot program (at least 200 comparisons possible!!)

## Slide 3
Novel loop filter design
Need: decoupling of dynamic performance and filtering characteristic
Error quantization
Damping optimization
Newton
Raphson
Cardan’s
Analytical
Solution
ωn
δ
Gives a unique set of loop filter parameters kp and ki - no trial and error

## Slide 4
3D lookup table: kp
3D lookup table: ki
Comparisons with Wiener method
  Better dynamic performance
  Extremely convenient from user’s perspective
Development of a 3D lookup table
  Theoretical aspect:
    Can be used as an educational tool to make notable inferences
  Practical aspect:
    Eliminate constraints on the speed and computing power of the micro-controller/ DSP
Novel filter design (continued)

## Slide 5
Conclusions
Analysis and in-depth understanding of 4 existing PLL schemes
Development of a generalized software applet
  Excellent learning tool
  Easy to use
  To find out which scheme tackles a particular issue better
  Additions of other schemes (if required) can be easily done
Novel self-consistent model based loop filter design
  No trial and error as a unique (kp , ki) pair for a particular grid condition
  Both error and damping is optimized
  3D lookup table for easy hardware implementation
Hardware implementation
  MSP430 Launchpad is used and the ADC and PWM modules are interfaced
  Yet to create a frequency excursion to test the SRF PLL implementation
Future work
  Use of the 3D lookup table for re-configurable filter design
  Hardware testing of the proposed design on the other PLL schemes

## Slide 6: Thank you

## Slide 7: Conventional SRF PLL
Back

## Slide 8: DDSRF PLL
Back

## Slide 9: DSOGI PLL
Back

## Slide 10: MCCF PLL
Back

## Slide 11: 4 PLLs simulated on a single model

## Slide 12: The grid simulator used to create imperfect grid conditions
Back

## Slide 13: Intuitive plot program results
Back

## Slide 14
Error quantization
Back

## Slide 15
Damping optimization
Back

## Slide 16: Filtering characteristic v/s Dynamic response
Back
Filtering →
Dynamic performance → Bandwidth
Wiener method: good trade-off between filtering and dynamic response
Proposed method: focus is on dynamic response

## Slide 17: Comparisons – SRF PLL on phase jump

## Slide 18: Comparisons
Wiener method
Proposed method
Back

## Slide 19: 3D lookup table – optimized δ

## Slide 20: 3D lookup table – optimized ωn

## Slide 21: 3D lookup table – optimized τ
Back